## Slide 1
Middle East Technical University
Department of Electrical and Electronics Engineering
Mesut Uğur
Development of an Integrated Modular Motor Drive (IMMD) System
31.05.2017

## Slide 2
Research Group
Research Fields
Renewable Energy
Power Quality
Smart Grids
Power Electronics
Electrical Machines
Events
Weekly seminars
Journal Club
Research League
Multi-disciplinary project
Undergraduate students
http://power.eee.metu.edu.tr

## Slide 3
Outline
What is IMMD?
Why IMMD?
Challenges
DC Link Capacitor Optimization
IMMD Design
Future Work

## Slide 4
Conventional Motor Drives
Drives are placed in a separate cabinet
  Increased volume, weight and cost
Connection with long cables
  Long cable effect, EMI problems

## Slide 5
Integrated Modular Motor Drives (IMMDs)
The motor drive is integrated to the motor back-end
Both the motor and the drive are modularized

## Slide 6
Motivation - Integration
Power density
Voltage overshoots
Motor lifetime

## Slide 7
Motivation - Modularization
Increased fault tolerance
Reduced voltage stress
Distributed heat dissipation

## Slide 8
Critical Applications
Electric traction: EVs, HEVs, Trains
Aerospace: Aircrafts, Space crafts

## Slide 9
Challenges
Fitting into a small volume requires size reduction and optimum placement of components.
  Passive component size reduction
  Heat sink size reduction
Cooling of both units should be achieved simultaneously.
  Achieve superior drive efficiency
  Heat distribution

## Slide 10
Challenges
Power and control electronics components are subjected to high temperature and vibration.
In case one module is in fault, torque balance should be ensured.

## Slide 11
Gallium Nitride (GaN) Power Semiconductors
Wide band-gap (WBG) power semiconductor devices
Low semiconductor loss: heat sink size is reduced
High operation frequency: passive component size is reduced
High speed device
Low Rds_on
Low Eon & Eoff
High junction temperature
Low Cin and Cout

## Slide 12
Gallium Nitride (GaN) Power Semiconductors
Parasitic components become significant
Careful layout design is required
Commercial availability
Low ratings
Reliability

## Slide 13
DC Link Capacitor Optimization
DC link capacitors constitute
20% of cost and weight
30% of volume
DC Link capacitor types
Aluminum electrolytic
Metal Film
Multilayer ceramic (MLCC)
Critical parameters
Capacitance per volume
RMS current per volume
Cost
ESL & ESR
Reliability & lifetime
Mechanical durability

## Slide 14
DC Link Capacitor Optimization
DC Link average current
DC Link ripple voltage
DC Link RMS current
Capacitor heating

## Slide 15
Analytical model
  RMS current
  Capacitance (ripple voltage)
  Heating
Interleaving
DC Link Capacitor Optimization

## Slide 16
Selection aspects
Selection algorithm
Results
DC Link Capacitor Optimization

## Slide 17
Results
DC Link Capacitor Optimization

## Slide 18
IMMD Design
Four three-phase inverter modules (two-series and two-parallel)
Power stage with cascode GaN FETs
Permanent Magnet Brushless DC (PM-BLDC) motor
Fractional Slot Concentrated Winding (FSCW) stator
Four three-phase modules
6 kW total output power
24 slot double layer stator
20 pole PM rotor
600V – 20A GaN FETs
Four 20μF, 450V capacitors
Specifications

## Slide 19
IMMD Design
Buraya bir çizim koyalım
Devre ve motor

## Slide 20
IMMD Design
Loss Characterization

## Slide 21
Future Work
Near future
An IMMD laboratory prototype is being developed with the given specifications. The aimed performance is:
Drive efficiency: 98.5%
Drive power density: 15 W/cm3
Increased fault tolerance
Motor housing for cooling (no heatsink)
Ultimately
An IMMD laboratory prototype is being developed with the given specifications. The aimed performance is:
Drive efficiency: 98.5%
Drive power density: 15 W/cm3
Increased fault tolerance
Motor housing for cooling (no heatsink)

## Slide 22
References
G. Lo Calzo et al., “Integrated motor drives: state of the art and future trends,” IET Electr. Power Appl., vol. 10, no. 8, pp. 757–771, Sep. 2016.
J. Wang, Y. Li, and Y. Han, “Integrated Modular Motor Drive Design With GaN Power FETs,” IEEE Trans. Ind. Appl., vol. 51, no. c, pp. 3198–3207, 2015.
J. J. Wolmarans, M. B. Gerber, H. Polinder, S. W. H. De Haan, J. A. Ferreira, and D. Clarenbach, “A 50kW integrated fault tolerant permanent magnet machine and motor drive,” PESC Rec. - IEEE Annu. Power Electron. Spec. Conf., pp. 345–351, 2008.

## Slide 23
Thank you !