## Slide 1
Mesut Uğur
ugurm@metu.edu.tr
Department of Electrical and Electronics Engineering
Middle East Technical University
DC Link Capacitor Optimization for Integrated Modular Motor Drives
21.06.2017
The 26th IEEE International Symposium on Industrial Electronics

## Slide 2
Outline
Introduction
IMMD Technology Review
DC Link Modeling
DC Link Capacitor Evaluation
Results
Conclusions
References

## Slide 3
Introduction
Drives are placed in a separate cabinet
  Increased volume, weight and cost
Connection with long cables
  Long cable effect, EMI problems
The motor drive is integrated to the motor
Both the motor and the drive are modularized
http://www.emersonindustrial.com

## Slide 4
IMMD Technology Review
Power density
Voltage overshoots
Motor lifetime
Increased fault tolerance
Distributed heat dissipation
Reduced voltage stress
Motivation
Critical Applications
Electric traction: EVs, HEVs, Trains
Aerospace: Aircrafts, Space crafts
https://www.afdc.energy.gov/vehicles/how-do-hybrid-electric-cars-work

## Slide 5
IMMD Technology Review
Small volume ?
Cooling ?
Vibration ?
Challenges
Wide band-gap (WBG) power semiconductor devices
Low loss: heat sink size is reduced
High speed: passive component size is reduced
Gallium Nitride (GaN)

## Slide 6
DC Link Capacitor Selection
DC link capacitors constitute
20% of cost and weight
30% of volume
DC Link model
Critical parameters
Capacitance requirement
RMS current
Thermal characteristics
Reliability & lifetime
Mechanical durability
Motivation

## Slide 7
DC Link Modeling
Analytical model

## Slide 8
Effect of interleaving
DC Link Modeling
Minimum RMS current is achieved at for even number
It is not practical to use number of modules higher than 4

## Slide 9
DC Link capacitor types
DC Link Capacitor Evaluation
Metallized Polypropylene Film Capacitors
Aluminum Electrolytic Capacitors
Multi-Layer Ceramic Capacitors (MLLC)

## Slide 10
Capacitor selection aspects
DC Link Capacitor Evaluation
The basic parameters
• Capacitance due to voltage ripple
• RMS current due to current ripple
• Voltage due to topology
The major concerns
• High power density
• Low height
• Low cost
• Low temperature sensitivity
• Mechanical durability
• Lifetime
Metallized Polypropylene Film Capacitors
https://en.tdk.eu/inf/20/20/db/fc_2009/MKP_B32674_678.pdf

## Slide 11
Capacitor selection algorithm
DC Link Capacitor Evaluation

## Slide 12
Results
RMS current vs ma
Capacitance vs fsw
System Parameters |  | Constraints | 
Power factor | 0.9 | Power density | 10W/cm3
Vdc | 400V | Cost | 35$
Phase shift | 900 | Height | 35mm
Power per module | 2kW | Temp. rise | 5 0C
Ambient temp. | 40 0C | Vdc,r,pp | 1%
Max. RMS current
Only 30% reduction from 100kHz to 200kHz

## Slide 13
Results
10 μF, 300 V
2s, 10p
High cost
Low power density
40 μF, 300 V
2s, 3p
Moderate cost
Low power density
Height
40 μF, 450 V
1s, 2p
Height
High temp. rise
20 μF, 450 V
1s, 4p
High power density
Low cost
Low height
Low temp. rise

## Slide 14
Conclusions
Power density !
Size reduction challenge
Passive components and heatsink
GaN FETs
Optimize the DC bus capacitor bank
Interleaving is applicable
Optimum number of modules
Film capacitors are suitable
Consider all the aspects
Switching frequency limit
Sonuçlarla ilgili yorumlar

## Slide 15
Conclusions
Integrated modular motor drives
  Advantages and challenges
Volume reduction challenge
  DC link capacitor size optimization
DC Link model of an IMMD
  Critical parameters
  Analytical model
Interleaving
  Optimum phase shift angle
  Optimum number of modules
Capacitor selection algorithm
  Film capacitors => datasheet parameters
  Critical switching frequency
  Case results => optimum combination

## Slide 16
References
G. Lo Calzo et al., “Integrated motor drives: state of the art and future trends,” IET Electr. Power Appl., vol. 10, no. 8, pp. 757–771, Sep. 2016.
J. Wang, Y. Li, and Y. Han, “Integrated Modular Motor Drive Design With GaN Power FETs,” IEEE Trans. Ind. Appl., vol. 51, no. c, pp. 3198–3207, 2015.
J. J. Wolmarans, M. B. Gerber, H. Polinder, S. W. H. De Haan, J. A. Ferreira, and D. Clarenbach, “A 50kW integrated fault tolerant permanent magnet machine and motor drive,” PESC Rec. - IEEE Annu. Power Electron. Spec. Conf., pp. 345–351, 2008.
N. R. Brown, T. M. Jahns, and R. D. Lorenz, “Power Converter Design for an Integrated Modular Motor Drive,” Ind. Appl. Conf. 2007. 42nd IAS Annu. Meet. Conf. Rec. 2007 IEEE, pp. 1322–1328, 2007.
S. M. Lambert, B. C. Mecrow, R. Abebe, G. Vakil, and C. M. Johnson, “Integrated Drives for Transport - A Review of the Enabling Electronics Technology,” IEEE Veh. Power Propuls. Conf., pp. 1–6, 2015.
A. Shea and T. M. Jahns, “Hardware integration for an integrated modular motor drive including distributed control,” in 2014 IEEE Energy Conversion Congress and Exposition (ECCE), 2014, pp. 4881–4887.

## Slide 17
Thank you !
Mesut Uğur
ugurm@metu.edu.tr
Department of Electrical and Electronics Engineering
Middle East Technical University