## Slide 1
Literature Survey
for
IMMD Ver.2 Design
Mesut Uğur
06/10/2018
mesut.ugur@metu.edu.tr

## Slide 2
Fault Tolerant topologies for 3-phase drives
The product of the number of switches and the rating of each switch (V·I) is increased by a factor 1.15 compared to conventional
Redundant bridge arm
Solution with less switch number
Conventional
A phase can be completely short circuited to limit the short circuit current in case of a turn to turn short circuit fault, while it is still possible to control the two remaining phases.

## Slide 3
Traction ?
Pirius
Machine Volume: 4.774 l
Power density: 10.47 kW/l (peak power)
Speed: 6000 rpm
Our design
Machine Volume: 7.729 l
Power density: 1.04 kW/l (peak power)
Speed: 600 rpm
Coincidence ?
What are the limations for us for designing a high speed machine ?
Water cooling (high power)
Test setup
Mechanical parts
Tip speed
Core loss
Winding extra losses, litz wire?

## Slide 4
High speed design
We are here !

## Slide 5
High speed design
As the speed increases (same power):
Torque ↓
Dimensions ↓
Pole area ↓
Flux ↓ (13 kat)
Frequency ↑ (50 kat)
Coil voltage ↓ (3.5 kat)
Number of turns ↓ (3.5 kat)
Bu tasarımda aynı DC Link voltajı ve aynı modül sayısı var. Bu durumda faz gerilimi sabit. Tork çok düşmesine rağmen aynı akım var drive’da. Haliyle verimi hep aynı gidiyor.
Question: Böyle mi olmalı ?
Bu analizlerde core loss yok, yani aslında var da frekanstan etkilenmiyor.

## Slide 6
High speed design
Derken GaN’ları içeren şöyle bir analiz yaptım:
60A GaN bölgesi
30A GaN bölgesi
En düşük 24A, en yüksek 10A faz akımı var.
Hesap: Tepe akımı x 1.5 kat marjin
Question: 60 Amperlik GaN kullansam hep, ne olur?
60A GaN bölgesi
30A GaN bölgesi

## Slide 7
High speed design
Farklı transistör seçimleri:
Margin: 2
Margin: 1.2
60A GaN bölgesi
30A GaN bölgesi
60A GaN bölgesi
30A GaN bölgesi

## Slide 8
High speed design
Loss dağılımları:
Core loss’u hesaplayabilmeliyiz !

## Slide 9
High speed design
Volume and Power Density:
PCB’ye tüm komponentlerin sığdığı varsayılıyor !
Reduction in motor volume is obvious.
There is no change in the capacitor volume.
Drive volume reduces since the outer stator diameter reduces.
Heat sink required thermal impedance does not change.
Heat sink length increases since area is reduced.
In total, heat sink volume is decreased.