## Slide 1
Mesut Uğur
mesut.ugur@metu.edu.tr
Department of Electrical and Electronics Engineering
Middle East Technical University
Multi-physics Design Optimization of a GaN Based Integrated Modular Motor Drive System
04/18/2018
The 9th International Conference on Power Electronics, Machines and Drives

## Slide 2
Outline
Motivation (2’)
System model (3’)
Evaluation of design parameters (5’)
Optimum system design (2’)
Conclusions (2’)
References

## Slide 3
Motivation
Integrated Modular Motor Drive
Shea, A., & Jahns, T. M. (2014). Hardware integration for an integrated modular motor drive including distributed control. In 2014 IEEE Energy Conversion Congress and Exposition (ECCE) (pp. 4881–4887). IEEE.
Increased power density
Reduced cost
Reduced EMI
Fault tolerance
Redundancy
Reduced stress

## Slide 4
Motivation
Design Challenges
GaN Systems. (n.d.). GaN Systems E-mode GaN FETs. Retrieved January 15, 2018, from http://www.gansystems.com/
Marz, M., Schletz, A., Eckardt, B., Egelkraut, S., & Rauh, H. (2010). Power electronics system integration for electric and hybrid vehicles. Integrated Power Electronics Systems (CIPS), 2010 6th International Conference on, 16–18.
Wang, J. (2015). Design of Multilevel Integrated Modular Motor Drive with Gallium Nitride Power Devices. Thesis.
Multi-physics design optimization
Physical limitations: Thermal management, motor vibration
Structural limitations: Limited available space, converter height
Inter-dependencies between parts

## Slide 5
System Model
n
np
ns
fsw ma
α
ws
lm

## Slide 6
System Model
System Inputs
Constraints
Material properties
Ambient conditions
Datasheet values
Pout = 8 kW
Vdc = 540 V
Nr = 600 rpm
m = 3 phases
Cost function
Copper: AWG wire
Magnet: NdFe45H
Steel: M25035A
Arms = 35 kA/m
Bavg = 0.6 T
Jrms = 4 A/mm2
ηm = 96 %
ηd = 98 %
Vdc-r = 1 %
Tamb = 50 0C
Metallized Polypropylene Film Capacitors (MKP)
E-mode GaN FETs
Electrical
Thermal
Electromagnetic
Geometrical
Drive losses
Device temp.
Heat sink size
Thermal res.
Capacitor size
Power density
Efficiency
Material cost
Current
Rated voltage
Torque
Motor dimensions

## Slide 7
System Model
Interleaving
Power density
Magnetic equivalent circuit
Thermal equivalent circuit
DC Link
Motor dimensioning

## Slide 8
Design Parameter Evaluation
Switching frequency & Number of modules

## Slide 9
Design Parameter Evaluation
Modulation index & Number of modules

## Slide 10
Design Parameter Evaluation
Series and Parallel connection

## Slide 11
Design Parameter Evaluation
Number of slots/modüle/phase & Aspect ratio

## Slide 12
Optimum System Design
fsw = 50 kHz
ma = 0.9
GaN voltage ratings
Overmodulation
Tooth width
Manufacturing constraints
Drive component cost
Fault tolerance
Qs = 24
p = 20
α = 0.5
ws = 2
Drive efficiency: 98.3 %
Motor efficiency: 96.6 %
Power density: 0.71 kW/lt

## Slide 13
Conclusions
a
b
c

## Slide 14
References
[1] G. Lo Calzo, G. Vakil, B. Mecrow, S. Lambert, T. Cox, C. Gerada, M. Johnson, and R. Abebe, “Integrated motor drives: state of the art and future trends,” IET Electr. Power Appl., vol. 10, no. 8, pp. 757–771, Sep. 2016.
[2] M. D. Hennen, M. Niessen, C. Heyers, H. J. Brauer, and R. W. De Doncker, “Development and control of an integrated and distributed inverter for a fault tolerant five-phase switched reluctance traction drive,” IEEE Trans. Power Electron., vol. 27, no. 2, pp. 547–554, 2012.
[3] J. Wang, Y. Li, and Y. Han, “Integrated Modular Motor Drive Design With GaN Power FETs,” IEEE Trans. Ind. Appl., vol. 51, no. c, pp. 3198–3207, 2015.
[4] M. Ugur and O. Keysan, “DC link capacitor optimization for integrated modular motor drives,” 2017 IEEE 26th Int. Symp. Ind. Electron., vol. i, pp. 263–270, 2017.
[5] A. Shea and T. M. Jahns, “Hardware integration for an integrated modular motor drive including distributed control,” in 2014 IEEE Energy Conversion Congress and Exposition (ECCE), 2014, pp. 4881–4887.
[6] N. Bekka, M. E. H. Zaim, N. Bernard, and D. Trichet, “A Novel Methodology for Optimal Design of Fractional Slot with Concentrated Windings,” IEEE Trans. Energy Convers., vol. 31, no. 3, pp. 1153–1160, 2016.
[7] GaN Systems, “GaN Systems.” [Online]. Available: http://www.gansystems.com/. [Accessed: 15-Jan-2018].
[8] TDK, “Film Capacitors, Metallized Polypropylene Film Capacitors (MKP) - B32674...B32674 Datasheet,” no. May. 2015.
[9] R. E. Simons, “Estimating Parallel Plate-Fin Heat Sink Thermal Resistance.” [Online]. Available: https://www.electronics-cooling.com/2003/02/estimating-parallel-plate-fin-heat-sink-thermal-resistance/.

## Slide 15
Thank you !
Mesut Uğur
mesut.ugur@metu.edu.tr
Department of Electrical and Electronics Engineering
Middle East Technical University
power.eee.metu.edu.tr