## Slide 1
In conventional motor drive systems, drive units are placed in a separate cabinet, and they are connected to the motor via long cables. This brings increased volume and weight as well as increased voltage overshoot and electromagnetic interference (EMI) problems.
In integrated modular motor drives (IMMD), the motor drive is integrated directly to the motor back-end and the system is modularized by dividing into several parts [1].
Design of an Integrated Modular Motor Drive System
Introduction
Mesut Uğur Ozan Keysan
ugurm@metu.edu.tr keysan@metu.edu.tr
METU PowerLab
Department of Electrical and Electronics Engineering
Middle East Technical University
Powering the Energy Transition 2017
Motivation
Challenges
Integration
Power density of the overall system is enhanced significantly [2].
Voltage overshoots due to cabling effect is eliminated.
Fitting into a small volume requires size reduction and optimum placement of components.
Cooling of both units should be achieved simultaneously.
Power and control electronics components are subjected to high temperature and vibration [3].
DC link capacitor optimization
IMMD Design
References
G. Lo Calzo et al., “Integrated motor drives: state of the art and future trends,” IET Electr. Power Appl., vol. 10, no. 8, pp. 757–771, Sep. 2016.
J. Wang, Y. Li, and Y. Han, “Integrated Modular Motor Drive Design With GaN Power FETs,” IEEE Trans. Ind. Appl., vol. 51, no. c, pp. 3198–3207, 2015.
J. J. Wolmarans, M. B. Gerber, H. Polinder, S. W. H. De Haan, J. A. Ferreira, and D. Clarenbach, “A 50kW integrated fault tolerant permanent magnet machine and motor drive,” PESC Rec. - IEEE Annu. Power Electron. Spec. Conf., pp. 345–351, 2008.
Modularization
Fault tolerance is increased.
Voltage stress on modules is reduced.
Heat dissipation is distributed to a wider area.
Applications
Electric traction: electric vehicles, trains
Aerospace: aircrafts, space crafts
These challenges can be addressed by using wide band-gap (WBG) power semiconductor devices such as Gallium Nitride (GaN).
Low semiconductor loss: heat sink size is reduced
High operation frequency: passive component size is reduced
Additional challenges due to GaN
Parasitic components become significant
Careful layout design is required
DC link capacitors constitute:
20% of cost and weight,
30% of volume [1].
A set of film capacitors are considered. Optimization is achieved based on:
Power density
Cost
Height
Temperature rise
Effect of interleaving
Optimum phase-shift angle selection
Four three-phase inverter modules (two-series and two-parallel)
Power stage with cascode GaN FETs
Permanent Magnet Brushless DC (PM-BLDC) motor
Fractional Slot Concentrated Winding (FSCW) stator
Loss Characterization
Four three-phase modules
6 kW total output power
24 slot double layer stator
20 pole PM rotor
600V – 20A GaN FETs
Four 20μF, 450V capacitors
Specifications
DC link capacitor selection algorithm
Conclusions & Planned Work
An IMMD laboratory prototype is being developed with the given specifications. The aimed performance is:
Drive efficiency: 98.5%
Drive power density: 15 W/cm3
Increased fault tolerance
Motor housing for cooling (no heatsink)
DAAD Turkey