## Slide 1
Middle East Technical University
Department of Electrical and Electronics Engineering
Mesut Uğur
Development of an Integrated Modular Motor Drive (IMMD) System
31.05.2017

## Slide 2
Research Group
Research Fields
Renewable Energy
Power Quality
Smart Grids
Power Electronics
Electrical Machines
http://power.eee.metu.edu.tr
Events
Weekly seminars
Journal club
Research League
EEE Star program
Undergraduate students

## Slide 3
Outline
What is IMMD?
Why IMMD?
Challenges
DC Link Capacitor Optimization
IMMD Design
Future Work

## Slide 4
Conventional Motor Drives vs IMMD
Drives are placed in a separate cabinet
  Increased volume, weight and cost
Connection with long cables
  Long cable effect, EMI problems
The motor drive is integrated to the motor back-end
Both the motor and the drive are modularized

## Slide 5
Motivation
Power density
Voltage overshoots
Motor lifetime
Increased fault tolerance
Distributed heat dissipation
Reduced voltage stress

## Slide 6
Critical Applications
Electric traction: EVs, HEVs, Trains
Aerospace: Aircrafts, Space crafts
https://www.afdc.energy.gov/vehicles/how-do-hybrid-electric-cars-work
http://www.carparts.com/classroom/alternativepowersystems.htm

## Slide 7
Challenges
Small volume ?
Cooling ?
Vibration ?
  Passive component size reduction
  Heat sink size reduction
  Achieve superior drive efficiency
  Heat distribution

## Slide 8
Gallium Nitride (GaN) Power Semiconductors
Wide band-gap (WBG) power semiconductor devices
Low semiconductor loss: heat sink size is reduced
High operation frequency: passive component size is reduced
The total WBG device market is expected to be $743M in 2020 in a $12.7B overall market.
https://www.slideshare.net/Yole_Developpement/sic-sapphire-gan-what-is-the-business-evolution-of-the-nonsilicon-based-semiconductor-industry-presentation-held-by-on-semicon-west-2017-by-pierric-gueguen-from-yole-dveloppement

## Slide 9
DC Link Capacitor Selection
DC link capacitors constitute
20% of cost and weight
30% of volume

## Slide 10
DC Link Capacitor Selection
DC Link model
Analytical model
Critical parameters
Capacitance per volume
RMS current per volume
Cost
ESL & ESR
Reliability & lifetime
Mechanical durability

## Slide 11
Effect of interleaving
DC Link Capacitor Selection

## Slide 12
Effect of interleaving
DC Link Capacitor Selection

## Slide 13
Optimum phase shift angle for different number of modules
DC Link Capacitor Selection

## Slide 14
DC Link Capacitor Selection

## Slide 15
Results
RMS current vs ma
Capacitance vs fsw
Low voltage
Power density and cost is bad, superior thermal performance
High voltage
Low capacitance yields high cost
High capacitance yields bad thermal performance
Result:
4 25μF, 450V metal film capacitors connected in parallel

## Slide 16
IMMD Design
Four three-phase inverter modules
Power stage with cascode GaN FETs
Permanent Magnet Brushless DC motor
Fractional Slot Concentrated Winding
Four three-phase modules
6 kW total output power
24 slot double layer stator
20 pole PM rotor
600V – 20A GaN FETs
Four 20μF, 450V capacitors
Specifications

## Slide 17
How efficient?
Loss Characterization
IGBT: SKB15N60HS, 600V, 27A
4 modules
Pout = 6 kW
GaN: TPH3212PS, 650V, 26A
http://www.transphormusa.com/product/tph3212ps/http://www.transphormusa.com/product/tph3212ps/

## Slide 18
Future Work
Build a 6 kW laboratory prototype
Proof of concept
Drive efficiency: 98.5%
Drive power density: 15 W/cm3
Motor housing for cooling (no heatsink)
Fault tolerance tests

## Slide 19
References
G. Lo Calzo et al., “Integrated motor drives: state of the art and future trends,” IET Electr. Power Appl., vol. 10, no. 8, pp. 757–771, Sep. 2016.
J. Wang, Y. Li, and Y. Han, “Integrated Modular Motor Drive Design With GaN Power FETs,” IEEE Trans. Ind. Appl., vol. 51, no. c, pp. 3198–3207, 2015.
J. J. Wolmarans, M. B. Gerber, H. Polinder, S. W. H. De Haan, J. A. Ferreira, and D. Clarenbach, “A 50kW integrated fault tolerant permanent magnet machine and motor drive,” PESC Rec. - IEEE Annu. Power Electron. Spec. Conf., pp. 345–351, 2008.
N. R. Brown, T. M. Jahns, and R. D. Lorenz, “Power Converter Design for an Integrated Modular Motor Drive,” Ind. Appl. Conf. 2007. 42nd IAS Annu. Meet. Conf. Rec. 2007 IEEE, pp. 1322–1328, 2007.
S. M. Lambert, B. C. Mecrow, R. Abebe, G. Vakil, and C. M. Johnson, “Integrated Drives for Transport - A Review of the Enabling Electronics Technology,” IEEE Veh. Power Propuls. Conf., pp. 1–6, 2015.
A. Shea and T. M. Jahns, “Hardware integration for an integrated modular motor drive including distributed control,” in 2014 IEEE Energy Conversion Congress and Exposition (ECCE), 2014, pp. 4881–4887.

## Slide 20
Thank you !