## Slide 1
In conventional motor drive systems, drive units are placed in a separate cabinet, and they are connected to the motor via long cables. This brings increased volume and weight as well as increased voltage overshoot and electromagnetic interference (EMI) problems.
In integrated modular motor drives (IMMD), the motor drive is integrated directly to the motor back-end and the system is modularized by dividing into several parts.
Development of an Integrated Modular Motor Drive (IMMD) System
Introduction
Mesut Uğur Ozan Keysan
ugurm@metu.edu.tr keysan@metu.edu.tr
Department of Electrical and Electronics Engineering
Middle East Technical University
EEE Graduate Research Workshop 2017
Motivation
Challenges
Integration
Power density of the overall system is enhanced significantly.
Voltage overshoots due to cabling effect is eliminated.
Fitting into a small volume requires size reduction and optimum placement of components.
Cooling of both units should be achieved simultaneously.
Power and control electronics components are subjected to high temperature and vibration
DC link capacitor optimization
IMMD Design
References
G. Lo Calzo et al., “Integrated motor drives: state of the art and future trends,” IET Electr. Power Appl., vol. 10, no. 8, pp. 757–771, Sep. 2016.
J. Wang, Y. Li, and Y. Han, “Integrated Modular Motor Drive Design With GaN Power FETs,” IEEE Trans. Ind. Appl., vol. 51, no. c, pp. 3198–3207, 2015.
J. J. Wolmarans, M. B. Gerber, H. Polinder, S. W. H. De Haan, J. A. Ferreira, and D. Clarenbach, “A 50kW integrated fault tolerant permanent magnet machine and motor drive,” PESC Rec. - IEEE Annu. Power Electron. Spec. Conf., pp. 345–351, 2008.
M. D. Hennen, M. Niessen, C. Heyers, H. J. Brauer, and R. W. De Doncker, “Development and control of an integrated and distributed inverter for a fault tolerant five-phase switched reluctance traction drive,” IEEE Trans. Power Electron., vol. 27, no. 2, pp. 547–554, 2012.
Modularization
Fault tolerance is increased
Voltage stress on modules is reduced
Heat dissipation is distributed to a wider area
Applications
Electric traction: electric vehicles, trains
Aerospace: aircrafts, space crafts
These challenges can be addressed by using wide band-gap (WBG) power semiconductor devices such as Gallium Nitride (GaN).
Low semiconductor loss: heat sink size is reduced
High operation frequency: passive component size is reduced
Additional challenges
Parasitic components become significant
Careful layout design is required
DC link capacitors constitute 20% of cost and weight, and 30% of volume
An analytical model has been constructed. An algorithm has been developed. A set of film capacitors are considered. Optimization is achieved based on:
Power density
Cost
Height
Temperature rise
Effect of interleaving
Phase-shift angle
Proposed Topology
Series and parallel connected three-phase inverter modules
Fractional Slot Concentrated Winding (FSCW) stator
Permanent Magnet Brushless DC (PM-BLDC) motor
Winding diagram
Loss Characterisation
4 three-phase modules
24 slot double layer stator
20 pole rotor
600V – 20A GaN FETs
4 20uF, 450V capacitors, connected in parallel
Specifications